## Slide 1: ストレンジ・ダイバリオン探索実験に用いる 高時間分解能TOF検出器の開発
理化学研究所 仁科加速器センター
佐久間 史典
日本物理学会第71回年次大会 @ 東北学院大学 2016, 3/21
Development of a high-resolution TOF counter using MPPC array
for strange-dibaryon searches
RIKEN F.Sakuma
科研費 若手研究(B) 26800158

## Slide 2: Di-baryon (S=0)
Discovery of d* di-baryon
  WASA@COSY, PRL106(2011)242302
  p n  d p0 p0 (Tp=1.0/1.2/1.4GeV)
d*: s-channel resonance
m = 2.37 GeV, G = 68 MeV
t-channel DD contribution

## Slide 3: Di-baryon (S=-1)
KbarNN bound state?
  Still controversial…
J-PARC E15： K- 3He  L p n
(山我 21pAC-2)
E15?
Y. Sada, et al., arXiv:1601.06876 (PTEP accepted)

## Slide 4: Di-baryon (S=-2)
H di-baryon? (resonance?)
  Lattice-QCDs predict the existence, but…
  No experimental evidence so far
KbarKbarNN bound state?
  Theo. calcs. predict the existence
  No experimental search has been performed
p
p
K
K
S.Maeda, Y.Akaishi, T.Yamazaki
Proc. Jpn. Acad., B 89 (2013) 418.
Belle
PRL110,222022(2013).
experimental search via
pbar 3He  K+ K0 L L

## Slide 5: LL Measurement
pbar+3He annihilation at rest with 3NA processes:
aiming to search for
  KbarKbarNN with deep bound energy:
  H-dibaryon (resonance):
3He(stopped-pbar, LL) measurement would provide hints of S=-2 di-baryon
Gola of LL study
LL prod. rate
Study of IM(LL)
LL interaction

## Slide 6: J-PARC K1.8BR
S.Ohnish et al., PRC93, 025207
KbarN
Experiments to explore KbarN interaction
At the KbarN threshold:
Kbar-atom
Below the KbarN threshold:
L(1405)
KbarNN
KbarKbarNN
 E31
 E15
 E62/E57
 LoI
Sensitive in different energy region & isospin
川﨑
21aAW-6
山我
21pAC-2

## Slide 7: Cylindrical Detector System (CDS)
Improvement of PID in the CDS
  TOF with T0-CDH  change to DEF-CDH for p/Kstop exp.
  present DEF consists of WLS-fiber+MPPC (st~1ns)
   change to a high resolution detector (st<100ps)
AC
DC
T0
CDH
~50ps
~80ps
~1ns
DEF
-

## Slide 8: TOF Detector with MPPCs
Operation in magnetic field
Small & Compact
Cheep & Robust
High-Resolution (st<100ps)
Plastic scint. with MPPC
Multi-MPPCs
Series connection
Direct connection btw scint. and MPPCs
Fast pre-amplifire
Solution
Pioneer works:
MEG2 upgrade
MPPC holder
(3 MPPCs in series)
Connect MPPC folder and scint. with thin wires
S13360-3050CS
(3*3mm2)
Drill f0.5mm holes in a plastic scint.(EJ-230)
Rapping: ESR (3M)

## Slide 9: Fast Pre-Amplifier
HV out
in
HV in
out
+12V
(140mA)
8cm
4.5cm
HP MSA-0385
Fuji Diamond International Inc. 1504-S2
  1 ch/module
  HP MSA-0385 (Cascadable Silicon Bipolar MMIC Amplifier) x 2
  Pole Zero Cancellation
  Bandwidth (3dB):
  100kHz ~ 2GHz
  Dynamic Range (output):
  -2V ~ +2V
  Gain: 10~16 (depend on PZC)
  Noise: <10mV rms

## Slide 10: Pre-Test with Cosmic-Ray
Chart: Over-voltage/MPPC (V)
| 2.8 | 3.3 | 3.8 | 4.3
S12572-050C (t=5mm) | 106 | 95 | 97 | 114
S13360-3050C (t=5mm) | 88 | 81 | 80 | 74 | 73
2 types of MPPCs
  2nd gen. MPPC (S12572-050C)
  3rd gen. MPPC (S13360-3050CS)
CAMAC(ADC/TDC)+Kinoko
Cover Ratio: 27％
95mm
5mm
20mm
MPPC*3 (3mm2)
3rd gen. MPPC (S13360-3050C) has better performance
Vmax

## Slide 11: Beam-Test @ K1.8BR
Beam-test with 1 GeV/c p- @ K1.8BR beam-dump in Nov.-Dec., 2015
  length and thickness dependence
CAMAC(ADC/TDC)+Kinoko
~1000 trig./spill(5.5s)
[2*2mm2]

## Slide 12: Beam-Test @ K1.8BR
Beam-test with 1 GeV/c p- @ K1.8BR beam-dump in Nov.-Dec., 2015
  length and thickness dependence
CAMAC(ADC/TDC)+Kinoko
~1000 trig./spill(5.5s)
[2*2mm2]
ADC
slewing correction

## Slide 13: Results
st<80ps was achieved with the new DEF Counter
  sum of # of Npe > 100
  no position dependence of st
st~80 ps was achieved with “l~200mm (t=5mm)”
  st~100ps is expected with “l=300mm (t=5mm)”
L mm
5or3mm
20mm
MPPC*3 (3mm2)
Cover Ratio: (t=5mm) 27％
(t=3mm) 45%
Chart: length (mm)
| 45 | 90 | 145 | 195
t=5mm | 53 | 70 | 74 | 79
t=3mm | 75 | 77
New DEF

## Slide 14: New DEF
14mm
f168mm
Effective area:
96*100mm2
Design of the new DEF was completed
  all modules have been in hand
  will be installed in this year?
    depend on beam-time schedule @ K1.8BR

## Slide 15: Summary
A high-resolution TOF counter using MPPC array was developed for strange-dibaryon searches
  KbarNN (E15): K- 3He  L p n
  KbarKbarNN (LoI): pbar 3He  K+ K0 L L
A new Beam-Definition-Counter (DEF) was fabricated and we confirmed st to be <80ps
  A plastic scintillator (3*20*115mm3) with 3 MPPCs in series connection
  Also we achieved st~80ps with a l=200mm (t=5mmm) counter
Outlook:
  Pre-amplifire: integration in 1-module (~8 channels)
  Counter: test of a large size detector for a neutron counter, etc.
    c.f. NueLAND＠FAIR: 270*5*5cm3, 6mm2-MPPC*4, st<150ps

## Slide 17: Past Experiments of Double-Strangeness Production in Stopped-pbar Annihilation
experiment | Channel | # of events | yield (x10-4)
DIANA@ITEP [pbar+Xe] PLB464, 323 (1999). | K+K+X | 4 | 0.31+/-0.16
 | K+K0X | 3 | 2.1+/-1.2
OBELIX @CERN/LEAR [pbar+4He] NPA797, 109 (2007). | K+K+S-S-ps | 34+/-8 | 0.17+/-0.04
 | K+K+S-S+np- | 36+/-6 | 2.71+/-0.47
 | K+K+S-Ln | 16+/-4 | 1.21+/-0.29
 | K+K+K-Lnn | 4+/-2 | 0.28+/-0.14
Double strangeness production-yield: O(10-4)
No result of LL measurement so far

## Slide 18: Trigger
Simple multiplicity trigger in the CDS
Estimated trigger rate at 50 kW with Geant4.10 QGSP BERT physics list.
Trigger rate = ~1k/spill
NO problem!
SC: start counter

## Slide 19: Expected Yield & Sensitivity
Expected yield @ 50kW:
10-4 [LL/pbar] * 800 [pbar/spill] * 655 [spill/h] * 21 [h]
~ 1100 [LL/day]
* 0.01 [acceptance*Lpp-] * 0.7 [DAQ*ana] * 14 [days]
~ 110 [LL/2-weeks]
Sensitivity of LL
*S/N of LL is assumed to be 2.5
LL I.M.
R(H/K-K-pp) = 10-5/pbar
 N(H/K-K-pp) ~ 10/2-weeks
sensitivities of ~10-5 (3s)
LL~10-4/pbar