## Slide 1: J-PARCにおけるK中間子原子核探索実験のための円筒形ドリフト・チェンバーの開発II
理研
塚田暁
E15 experiment
CDS & CDC
Present status of CDC
Readout systems
Study of test chamber
summary
JPS meeting @ Yamagata Univ. 2008/09/21

## Slide 2: collaborations
理研, KEKA, 東大理B, 東大教養C, 京大理D, 阪大理E, 阪大RCNPF,
東工大理G,東理大理工H,大阪電通大I,Victoria大J, ソウル国立大K,SMIL,
ミュンヘン工大M, INFN-LNFN, INFN-TorinoO, Torino大P
塚田暁, 飯尾雅実, 板橋健太, 岩崎雅彦, 應田治彦, 大西宏明, 佐久間史典,
佐藤将春, 友野大, 山崎敏光, 石元茂A，岩井正明A, 鈴木祥仁A,
関本美知子A, 豊田晃久A, 石川隆B, 竜野秀行B, 鈴木隆敏B, 早野龍五B,
松田恭幸C, 永江知文D, 平岩聡彦D, 藤岡宏之D, 味村周平E, 阪口篤志E,
野海博之F, 藤原裕也G, 徳田真G, 千葉順成H, 福田共和I, 溝井浩I,
G. BeerJ, H.BhangK，S. ChoiK，H. YimK，石渡智一L,
P.BuehlerL, M. CargnelliL, A. HirtlL, P. KienleL,M, J. MartonL,
E. WidmannL, J. ZmeskalL, 岡田信二N, C. CurceanuN,
C.GuaraldoN, M. IliescuN, D. PietreanuN, D. SirghiN, F. SirghiN,
D. FasoO, O. MorraO, L. BussoP
JPS meeting @ Yamagata Univ. 2008/09/21

## Slide 3: E15 experiment
Search for the kaonic nuclear bound state
  Some experiments & theoretical calculations implies the existence of the bound state.
To clarify this question, we proposed the experiment detecting the formation & decay of the second simplest state.
Really? If exist, how?
Missing Mass detecting neutron
Invariant Mass for decayed particles
JPS meeting @ Yamagata Univ. 2008/09/21

## Slide 4: Experimental setup
1.0GeV
K- beam
23aSD-9
Y. Fujiwara will report about the Beam Line detectors.
K1.8BR beam line
CDS
3He
23pSN-4 & 23pSN-5
M.Iio and M. sato will report about the Liquid 3He target.
Sweep Magnet
KURAMA
Neutron counter array
15m
JPS meeting @ Yamagata Univ. 2008/09/21

## Slide 5: Cylindrical Detector System (CDS)
Target chamber
3He Target
Solenoid Magnet Yoke
Cylindrical
Detector Hodoscope
In production
Z-vertex Chamber
In production
Kaon Decay Counter
Under development
JPS meeting @ Yamagata Univ. 2008/09/21

## Slide 6: Cylindrical Drift Chamber (CDC)
Wires
  Sense : Au-W 30mm
  Field : Au-Al 100 mm
#sense wire : 1816
Shield layers among super layers
CFRP
t1mm
Alminum Support
×6
Layer# | Direction | #cells | Radius [cm] | Cell size [cm] | Tilt [deg]
1 | X | 72 | 19.05 | 0.83 | 0
2 | X’ |  | 20.4 | 0.89 | 0
3 | X |  | 21.75 | 0.95 | 0
4 | U | 90 | 24.85 | 0.87 | 3.72
5 | U’ |  | 26.2 | 0.91 | 3.92
6 | V | 100 | 29.3 | 0.92 | 3.95
7 | V’ |  | 30.65 | 0.96 | 4.12
8 | X | 120 | 33.75 | 0.88 | 0
9 | X’ |  | 35.1 | 0.92 | 0
10 | U | 150 | 38.2 | 0.80 | 3.43
11 | U’ |  | 39.55 | 0.83 | 3.55
12 | V | 160 | 42.65 | 0.84 | 3.59
13 | V’ |  | 44 | 0.86 | 3.71
14 | X | 180 | 47.1 | 0.82 | 0
15 | X’ |  | 48.45 | 0.85 | 0
JPS meeting @ Yamagata Univ. 2008/09/21

## Slide 7: Transition & present status of CDC
Mar 2008
CDC was completed and moved to KEK.
KEK
19 Aug 2008
CDC was moved to J-PARC.
9 Sep 2008
CDC was moved in the K1.8BR counting room.
J-PARC
We could supply the HV (a few 100 V) at last.
The aging procedure and more studies will be done from now
We could not use any electronics here.
We could not use any electronics here.
JPS meeting @ Yamagata Univ. 2008/09/21

## Slide 8: Readout systems
Amp card
  Chip : CXA3183Q (SONY, low noize ASD IC, t=16nsec)
  Output : LVDS differential
  Gain : 0.8V/pC at preamp
3 layers structure
Output
Analog out
All parts will be ready in September.
JPS meeting @ Yamagata Univ. 2008/09/21
1
2
3
HV board

## Slide 9: Readout system (2)
ASD
LVDS  ECL translation boards ( in the experimental hall )
TKO DrT modules ( in the counting room)
8m flat cables
60m flat cables to the K1.8BR counting room
In production

## Slide 10: Study using a test chamber
Corresponding to Layer#1 ~ 3
Gas : Ar-C2H6 (50:50)
Trigger : 2 plastic scintilator
TDC : CAMAC 2277
DAQ : unidaq
HV : 2600 V
JPS meeting @ Yamagata Univ. 2008/09/21
Spacial resolution < 200mm

## Slide 11: Tolerance for temperature
黒：６０℃
赤：７０℃
青：８０℃
紫：６０℃
TDC (test pulse)
center
RMS
1nsec
Heater
By thermocouple thermometer
ASD can work in the high temperature.
The timing change, but it is small (0.1nsec/10deg ).
JPS meeting @ Yamagata Univ. 2008/09/21

## Slide 12: Summary & Outlook
At the J-PARC K1.8BR beam line, we are constructing the dedicated detector system for the search of Kaonic nuclear bound state.
CDC was already moved to J-PARC, and more studies will be done in a few month.
  The test chamber shows good performance.
  Needed parts will be ready soon.
The installation method and jigs must be confirmed in this year.
  Design & Construction
JPS meeting @ Yamagata Univ. 2008/09/21

## Slide 13: Backup 1

## Slide 14: Backup 2

## Slide 15: Backup 3

## Slide 16: Backup 4
Bound state will be seen if exist.
  Cross section : 5 ~ 40 mb/(sr MeV)
  Resolution should be < 20 MeV
J. Yamagata, S. Hirenzaki, H. Nagahiro, D. Jido, Mod. Phys. Lett. A accepted. Proc. of Chiral07.
T. Koike, T. Harada, Phys. Lett. B652 (2007) 262
Deep Potential
Shallow Potential

## Slide 17: Readout systems (2)
8m cable
Repeater
50m cable
TKO DrT in the counting house